Script for

Saving Home Energy and Heating Costs

Low Cost / No Cost Ideas to Help Yourself

Part 2

- Saving Home Energy and Heating Costs with low cost and no cost ideas to help yourself.

- Let’s look at how we can save energy and be more comfortable in our homes this winter.  Some things will cost nothing, some will have a little expense, some ideas will cost more and some options might be too costly to be able to benefit from the initial expense. If you will notice the upper left corner of the slide is a marker that will be placed on slides to indicate this activity or item is appropriate for apartment dwellers as well as home owners.

- There are a number of things that can impact how comfortable we feel in terms of heat or warmth.  Human Thermal Comfort is affected by the air temperature, air velocity or drafts, relative humidity, where too much can cause us to feel clammy and too little can lead to dry skin.  Also clothing, metabolic rate or level of activity and the mean radiant temperature can contribute to our thermal comfort.

- There are a number of things that we can do differently on a personal basis to keep warm, comfortable and save energy through this winter.  Don’t sit around in summer clothes and think you will be comfortable! Get out your sweaters, sweatshirts, lap quilts, etc. to be comfortable. Taking short showers instead of baths will save hot water.  Remind others in the home to be sure to shut the door tightly behind them when coming in or going out of the house.  If you have children impress upon them how important it is to try to save energy this winter.

- To keep warm and save energy turn down the thermostat when you leave the house and at night. A programmable thermostat can do it for you so you won’t forget.  Every fall check heating vents to be sure they are clean.  Don’t forget to check the return air ducts in forced hot air systems to be sure they are clean.  Also opening drapes in south facing windows during the day will increase the solar gain in the room, closing them at night will reduce heat loss.

- Have your furnace or boiler cleaned and serviced annually. Clean hot air furnace filters monthly or as often as recommended. Hot air ducts should be sealed with foil tape not duct tape since duct tape will deteriorate too quickly.  Boilers provide heat to hot water systems and convectors provide heat to the home.  Be sure the space at the bottom of the convector is not blocked. Vacuuming the fins behind the convectors annually will improve efficiency.   Use caution when thinking about closing off unused rooms if you have a hot water heating system.  If the temperature gets too cold the pipes may burst causing expensive repairs.  This isn’t a concern with rooms heated by hot air that don’t have any plumbing fixtures in them. If you have ceiling fans be sure to change the direction of the rotation to winter settings to improve the comfort level in your home.

- Reducing air infiltration that can cause drafts will give you a big bang for your buck in terms of heat saved and increased comfort.  There are a number of ways to reduce air infiltration including insulation and caulking and weather stripping.  You don’t have to be a pro to check for drafts in your home.  If you have lived in your home through a winter and experienced the effects of winter winds making your curtains move in the windows, you know there is a draft problem there.  If you sit by an outlet and feel that cool blast of air, you have a draft problem.  You can also use a piece of tissue paper taped to a pencil to detect drafts. Turning on the bathroom or kitchen exhaust fan will make the air movement more obvious.

- To stop drafts associated with outlets there are special foam gaskets that can be easily installed in your outlets and light switches with the use of a screw driver. First turn off your power so you won’t get shocked.  Unscrew the screw, remove the outer plastic cover, put the gasket in place, return the plastic outer cover and screw back in place.

- Stopping air infiltration will greatly improve the comfort of your home by stopping the cool drafts that can chill you.  Caulking the largest holes first including those around wiring, pipes and duck penetrations in the attic, under the floor and through walls.  Weatherize your doors and windows with caulk or weather stripping.  Installing a vapor barrier such as a piece of plastic on the warm side of insulation will also help reduce air infiltration.

- How do you caulk?  If you have used tube frosting to make a design on a cake you can use a caulking gun.  You lay down a bead of caulk around windows, around the foundation, or any place that has a gap to the out doors.  If it looks a little ragged you can smooth it with your finger or piece of plastic. Caulking will last several years.  There are a number of different types of weather striping for doors and windows.  Caulking and weather stripping will pay back in reduced heating bills in one year.

- Installing storm windows and banking on the house will also help reduce air infiltration, especially with the old rock foundations.  Homes with vinyl siding need to use something that doesn’t need to be nailed in place like bags of leaves, bales of straw or solid foam board.  Remember do not to cover vents from any propane fired appliances with banking materials.

- Of course if at all possible adding insulation and vapor barriers to the inside of the  basement or crawl space wall of you home will make these improvements permanent and then you can eliminate the annual fall chore of banking the house.

- During cold nights hot air from the ceiling of a room will move to the edge of the room and start going down the wall.  If this warm air passes over a window (even with drapes closed) it is immediately cooled and will fall to the floor causing a draft.  Curtains are more effective if they have a header board or cornice at the top of the window to prevent the precious warm air from moving down next to the cold window and causing a draft at the bottom of the window.

- Window treatments need to be portable and easy to use to really be effective.  We can use heavy curtains, roman shades with fiber fill and plastic sheeting, rigid Styrofoam board or you can make your own tight fitting window shutter out of cardboard, aluminum foil, duct tape and foam weather stripping.   UMaine Extension has factsheets that outline how to make these window treatments.

- With a little cloth and foam pipe insulation or sand, you can make door draft stoppers or window draft snakes to reduce air infiltration and make you more comfortable. If you are not a crafty person you can stuff a few plastic bags inside another plastic bag and use to seal a window.   This door draft stopper will stay with the door when it is opened and closed. Again UMaine Extension has a how to factsheet on making these items.

- Heating water takes a lot of energy and we keep a big tank of hot water ready all day long for the few minutes that we want to use it.  Turn down the temperature on your water heating system whether it is oil, gas or electrically powered to 120 degrees.  Annually drain a few gallons of water out of the bottom of your water heater to remove any rusty deposits to increase the longevity and efficiency of your heater.  Installing low flow showerheads and stopping any faucet leaks will reduce your energy use.  Insulate any hot water supply pipes with the foam pipe insulation material. Also, some hot water heater themselves can be insulated but check the manufacturer information since applying extra insulation may void warranty.

- Did you know that many televisions are not off when we turn them off?  They continue to draw power to be ready to turn on instantly when we want to watch television. This is sometimes called phantom power. All the other electronics connected to the television, satellite, video player, cable box, etc. may all be drawing power 24/7.  You local library has a Kill-A-Watt meter that you can borrow to see how much your appliances continue to draw power when turned off. To stop this continuous power draw plug these things into a power strip and flick the switch off when you are done watching your favorite shows. Compact florescent bulbs can save on dollar per month compared to incandescent bulbs.  And of course, if you aren’t in the room, turn the light off.

- When we think about lighting energy use there are two things to consider.  The energy used and the light produced.  Energy used is expressed as watts.  We used to like a 75 watt incandescent bulb to read by since it would produce over 1,000 lumens of light.  But a 20 watt compact florescent bulb is a great investment that can give us this same amount of light at one dollar per month savings for each bulb we replace.  Also, they will last 10 times longer than our old incandescent bulbs.  There are some cautions that need to be followed when these bulbs break since they have a minute amount of heavy metal in them.  Maine has a CFL bulb recycling program where many retailers provide bins for recycling these bulbs.

- Holiday lighting has a new energy efficient light source, “Light Emitting Diodes” or LEDs.  As you can see it will pay to replace your holiday lights with this new product. In this example the homeowner is using 500 feet of different lights for 6 hours each night for 40 nights.  Of course you could reduce the hours your lights are lit or you could change from the very old C7 bulbs that would cost $134 a season and the common mini incandescent bulbs that would cost $34 a season to the new LED at $3 to $4 a season.   Look for LEDs to be used in the home in place of the compact florescent bulbs as the next generation of lighting technology.

- Refrigerators and freezers use the most energy in our kitchen because they are on all the time.  To make them more efficient clean their coils, remove any frost if you don’t have a frostless appliance.  To check the gaskets, place a dollar bill on the gasket of the refrigerator, close the door and try to pull the dollar out.  If it comes out easily, you are losing energy, replace the gasket. Also, keeping the refrigerator or freezer filled is more efficient.  You can fill soda bottles with water to take up space in your freezer.  Any time you replace an appliance be sure to purchase ENERGY STAR™ rated appliances that are more energy efficient.

- We have a variety of ways we can cook foods for our families.  We each have a favorite method.  As you can see some methods are more energy efficient than others.  Before you turn on your large oven to bake something consider cooking other items in the oven at the same time or consider using the toaster oven if possible since it uses about half the energy of the large oven.  The microwave is the most efficient method of heating foods but might not be appropriate for every recipe.

- Other energy saving techniques in the kitchen include using the smallest pot on the smallest burner.  Don’t use your tiny pot to boil and egg on your large burner.  It can damage the handle of the pot as well as waste a lot of energy. Use the lid on your pots to conserve heat. Don’t be peaking into the oven all the time checking on the progress of your meal.  The oven has to reheat all the cool air that you let into the oven when you open the door.

- If you have a dish washer run it only when full, don’t pre-rinse since they are made to wash all that sticky food stuff off your dishes.  When washing by hand don’t leave the faucet running all the time, wash the dishes, put in a dish rack and then rinse them all at once.

- We now have detergents that will work in cool water. Unless you have extremely dirty clothes, you should be using cool water wash and rinse.  Wait till you have a full load to wash before starting up the washer. Also, don’t over dry your clothes or better yet why not hang them out on a nice day to dry in the sun.  Drying clothes in the home during the winter can add humidity to the dry air in your home while saving some energy.

- Next we will move into some suggestions for energy saving that may cost a little to install but will give big returns.  If you have a fireplace remember your damper may not block off the air leakage up your chimney so installing a tight fitting set of doors will help.  There are new fireplace inflatable plastic pillows that will seal the fireplace when not in use. But these can be a safety hazard.  Try hanging something down in your fireplace to remind you that something is blocking the chimney. Also, be sure to check the chimney before you start a fire since wildlife may have set up housekeeping in your chimney.

- Many times we start the winter planning to turn the thermostat up and down based on when we are in the home.  In reality, we tend to forget to turn the thermostat down when we don’t need to heat the home at night or when we are away at work.  The answer is a programmable thermostat.  Set it to come up to a comfortable temperature before you get up in the morning or home from work. The cost is between $50 and $100 and can return 1% of your annual heating bill for every degree you set back for eight hours. Do you still have an old mercury thermostat?  Efficiency Maine and the Maine Department of Environmental Protection have a mercury thermostat recycling program.  Just bring your old thermostat into your hardware store and get a $5 store credit towards a new one.

- Homeowners with forced hot air heating systems need to be very aware about leaks in the air ducts of their systems.  Yes, duct tape was originally made to hold the air ducts together, but the foil backed tape lasts longer and does a better job.  You can also add insulation to the ducts that run through unheated air spaces to conserve the heat they carry.

- If you are ready to make a more significant investment in energy saving items consider insulation your first investment option if your home isn’t up to the recommended R-values. You know which windows and doors leak the most. Consider replacing one or two a year until they are all done. If you have an old heating system it may be time to upgrade or supplement with a different type of system. This slide shows how to calculate the cost and benefit of installing some insulation in an attic space to bring it up to an R-47.  The 15% savings in heating costs would be paid for in two and a half years in this example.

- Insulation video with Kathy Hopkins.

- One caution about insulating your attic space.  To prevent ice dams be sure you have enough insulation and ventilation to keep your roof cold.  You don’t want to heat the roof, you want to keep the heat in your living space.  Passive ventilation is achieved through proper sizing of vents at the eaves and roof.  This can help reduce the formation of ice dams.

- There are a number of certifying organizations that rate the relative efficiency of appliances, heating or cooling systems, and building materials.  Look for these ratings when you shop for replacements for your home.

- You can use the Annual Fuel Utilization Efficiency rating of your old furnace or boiler and compare it to the AFUE rating of a new furnace or boiler the figure out how much money you can save per $100 of annual fuel costs.  In this example the old 65% efficient furnace is replaced with a 90% efficient furnace so the home owner would save $28 per $100 of fuel costs per year. The Federal tax incentive program is based on AFUE ratings.

- You can calculate your return on investment in a new heating system by taking the annual savings of the new system divided by the initial cost of the system and multiply the result by 100 to get the percent return on investment.  If you spent $3,800 per year on fuel you would save $1,064 per year with the new heating system. In this case the family will receive 21% return on their investment in a new heating system.  With banks paying less than 1% for your savings dollars it makes sense to invest in a new heating system.

- To help give you incentives to implement these energy conservation techniques there are a number of programs available.  The Home Energy Loan program assists low income people with energy efficiency improvements.  And finally the federal government will allow you to deduct from your tax obligation up to $1,500 in energy conservation improvements at the rate of 30% of the cost of the materials for the next two years combined.  Materials eligible for the tax incentive have been certified by the manufacturer and ENERGY STAR™.  It does not include the cost of installation.  To view all energy incentive program you can go to www.dsireusa.org.

- If you have access to the internet here are several web sites to visit.  Stay tuned for Part 3 Comparing Different Home Heating Fuels and Alternative Energy Systems.

Developed by UMaine Cooperative Extension Associate Extension Professors Donna Coffin and Kathy Hopkins. Reviewed by Joy Adamson and Richard Bacon, Efficiency Maine Program Managers, Maine Public Utilities Commission. 2009.